## Slide 1
Fundamentals of Information Science:
Part 3: Coding Technologies
Shandong University
2025 Spring

## Slide 2: Channel Capacity

## Slide 3: Channel Coding Theorem

## Slide 4: Asymptotically Error-free at R < C

## Slide 5
Lecture 2.2 : Linear Block Codes

## Slide 6: Channel Coding

## Slide 7: Hamming Distance

## Slide 8: Idea： Embedding for Structural Separation

## Slide 9: Minimum Hamming Distance of Codes vs. Detection & Correction Capabilities

## Slide 10: Minimum Hamming Distance

## Slide 11: How to Construct Codes

## Slide 12: A Simple Code: Parity Check

## Slide 13: Binary Arithmetic

## Slide 14: Linear Block Codes

## Slide 15: Linear Block Codes

## Slide 16: Minimum HD of Linear Code

## Slide 17: Examples: What are n, k, d here?

## Slide 18: (n, k) Systematic Linear Block Codes

## Slide 19: Generator Matrix of Linear Block Code

## Slide 20: (n, k) Systematic Linear Block Codes

## Slide 21: How Many Parity Bits Do We Need?

## Slide 22: Hamming Codes

## Slide 23: (7, 4, 3) Hamming Code

## Slide 24: Logic Behind Hamming Code

## Slide 25: Syndrome Decoding: Idea

## Slide 26: Constraints for more than single-bit errors

## Slide 27: Elementary Combinatorics

## Slide 28: Error-Correcting Codes occur in many other contexts

## Slide 29
Linear Block codes - Basis

## Slide 30
Example: (7, 4) Hamming Code

## Slide 31
Example: (7, 4) Hamming Code

## Slide 32
Hamming Code – Parity Checks

## Slide 33
Hamming Code – Matrix Perspective

## Slide 34
Parity-Check Equations

## Slide 35
Evolution of Channel Coding
1948
Hamming Code
1955
Convolution Code
Peter Elias
(1923-2001)
Andrew J. Viterbi
(1935-)
1967
Viterbi Decoding
Claude Berrou
(1951-)
1993
Turbo Code
3G/4G
Irving Reed
（1923-2012)
1960
Reed-Solomon Code
Richard Hamming
(1915-1998)

## Slide 36
Asymptotically (near) optimal coding (5G)
Robert Gallager
(1931-)
1962年发明LDPC码
埃达尔·阿利坎
Erdal Arikan
(1958-)
2008年发明Polar码

## Slide 37
Lecture 2.3 : Reed-Solomon Codes, BCH Codes

## Slide 38: Nonbinary single error correcting code

## Slide 39: More equations needed

## Slide 40: Decoding procedure

## Slide 41: Finite Fields

## Slide 42: Reed-Solomon codes

## Slide 43: Galois Field
Definition: Field: a complete group of elements with:
  Addition, subtraction, multiplication, division
  + - * /
  Completely closed under these operations
  Every element has an additive inverse
  a + b = 0
  Every element except zero has a multiplicative inverse
  a * b = 1

## Slide 44: Galois Field Examples
  Real numbers
  Binary, called GF(2)  Galois Field with base 2
    Values 0, 1. Addition/subtraction: use xor. Multiplicative inverse of 1 is 1
  Prime field, GF(p)  Galois Field with base p
    Values 0 … p-1
    Addition/subtraction/multiplication: modulo p
    Multiplicative Inverse: every value except 0 has inverse
    Example: GF(5): 11  1 mod 5, 23  1mod 5, 44  1 mod 5
  General Galois Field: GF(pm)  base p (prime!), dimension m
    Values are vectors of elements of GF(p) of dimension m
    Add/subtract: vector addition/subtraction
    Multiply/divide: more complex
    Just like real numbers but finite!
    Common for computer algorithms: GF(2m)

## Slide 45: Galois Field Examples GF(2n)
Consider polynomials whose coefficients come from GF(2).
Each term of the form xn is either present or absent.
Examples: 0, 1, x, x2, and x7 + x6 + 1
= 1·x7 + 1· x6 + 0 · x5 + 0 · x4 + 0 · x3 + 0 · x2 + 0 · x1 + 1· x0
With addition and multiplication these form a “ring” (not quite a field – still missing division):
“Add”: XOR each element individually with no carry:
x4 + x3 + + x + 1
+ x4 + + x2 + x
x3 + x2 + 1
“Multiply”: multiplying by x is like shifting to the left.
x2 + x + 1
 x + 1
x2 + x + 1
x3 + x2 + x
x3 + 1

## Slide 46: What about division (mod)
x4 + x2
x
= x3 + x with remainder 0
x4 + x2 + 1
X + 1
= x3 + x2 with remainder 1
x4 + 0x3 + x2 + 0x + 1
X + 1
x3
x4 + x3
x3 + x2
+ x2
x3 + x2
0x2 + 0x
+ 0x
0x + 1
+ 0
Remainder 1

## Slide 47: Galois Fields
These polynomials form a Galois (finite) field if we take the results of this multiplication modulo a prime polynomial p(x)
A prime polynomial cannot be written as product of two non-trivial polynomials q(x)r(x)
For any degree, there exists at least one prime polynomial. With it we can form GF(2n)
Every Galois field has a primitive element, , such that all non-zero elements of the field can be expressed as a power of 
Certain choices of p(x) make the simple polynomial x the primitive element. These polynomials are called primitive
For example, x4 + x + 1 is primitive. So  = x is a primitive element and successive powers of  will generate all non-zero elements of GF(16).
Example on next slide.

## Slide 48: Galois Fields with primitive x4 + x + 1
0 = 1
1 = x
2 = x2
3 = x3
4 = x + 1
5 = x2 + x
6 = x3 + x2
7 = x3 + x + 1
8 = x2 + 1
9 = x3 + x
10 = x2 + x + 1
11 = x3 + x2 + x
12 = x3 + x2 + x + 1
13 = x3 + x2 + 1
14 = x3 + 1
15 = 1
Primitive element α = x in GF(2n)
In general finding primitive polynomials is difficult. Most people just look them up in a table, such as:
α4 = x4 mod x4 + x + 1
= x4 xor x4 + x + 1
= x + 1

## Slide 49: Primitive Polynomials
x12 + x6 + x4 + x +1
x13 + x4 + x3 + x +1
x14 + x10 + x6 + x +1
x15 + x +1
x16 + x12 + x3 + x +1
x17 + x3 + 1
x18 + x7 + 1
x19 + x5 + x2 + x+ 1
x20 + x3 + 1
x21 + x2 + 1
x22 + x +1
x23 + x5 +1
x24 + x7 + x2 + x +1
x25 + x3 +1
x26 + x6 + x2 + x +1
x27 + x5 + x2 + x +1
x28 + x3 + 1
x29 + x +1
x30 + x6 + x4 + x +1
x31 + x3 + 1
x32 + x7 + x6 + x2 +1
x2 + x +1
x3 + x +1
x4 + x +1
x5 + x2 +1
x6 + x +1
x7 + x3 +1
x8 + x4 + x3 + x2 +1
x9 + x4 +1
x10 + x3 +1
x11 + x2 +1

## Slide 50: Primitive Polynomials
Galois Field Hardware
Multiplication by x  shift left
Taking the result mod p(x)  XOR-ing with the coefficients of p(x)
when the most significant coefficient is 1.
Obtaining all 2n-1 non-zero
elements by evaluating xk  Shifting and XOR-ing 2n-1 times.
for k = 1, …, 2n-1

## Slide 51: Reed Solomon Codes
Galois field codes: code words consist of symbols
  Rather than bits
Reed-Solomon codes:
  Based on polynomials in GF(2m) (I.e. m-bit symbols)
  Data as coefficients, code space as values of polynomial:
  P(x)=a0+a1x1+… ak-1xk-1
  Coded: P(0),P(1),P(2)….,P(n-1)
  Can recover polynomial as long as get any k of n

## Slide 52: Example
Galois field GF(4)
Reed-Solomon Code with n=q=4, k=2
Full coding map:

## Slide 53: The Singleton bound and MDS codes
The Singleton bound: fundamental bound on (n, k, d) over any field:
        k + d <= n + 1
Proof: The code can correct any set of d-1 erasures.
Erasing the last d-1 symbols, the codewords are different.
Number of codewords <= qn-d+1
MDS codes: A code that meets this bound with equality is called “maximum distance separable” (MDS).
Reed-Solomon Code is an MDS code

## Slide 54: Decoding of Reed-Solomon Codes
Reed-Solomon codes can be decoded rather easily using finite-field arithmetic.
Decoding algorithms such as Peterson, Berlekamp-Massey, Euclid, and Welch-Berlekamp have been developed for error-correction and erasure-and-error correction.
Sudan and others have derived list and soft-decision error-correction algorithms that can decode significantly beyond the guaranteed error-correction capability
Polynomial-time, most efficient requiring the order of n2 finite-field operations

## Slide 55
Applications of Erasure Coding
File transmission (code on file blocks)
Disk Failures (Redundant Array of Independent Disks)

## Slide 56
Applications of Erasure Coding
Distributed File System (Azure, Hadoop 3.0)
vs. 3 replications

## Slide 57
Applications of Erasure Coding
Distributed File System (Azure, Hadoop 3.0)
vs. 3 replications

## Slide 58
Reed-Solomon Code
Codewords satisfies

## Slide 59
Bose–Chaudhuri–Hocquenghem (BCH）codes
Codewords satisfies
odd
Codewords are in field GF(2)
Orders are odd

## Slide 60
BCH codes
Why do we choose odd ?

## Slide 61
BCH codes
m=8, n=255
Parity checks: 8*t
k = 255 – 8 *t

## Slide 62
BCH codes Applications
Telecommunication
SSD